## Slide 1
<number>
ITU
(International Telecommunication Union)
ITU-T
(Telecommunication standardization sector)
Study Group 12
(Performance, QoS and QoE)
Overview of Multimedia Assessment Activities in ITU-T Study Group 12
QoMEX’10, Trondheim, Norway
Alexander Raake, Jörgen Gustafsson Co-Rapporteurs Q.14/12
Notes: <number>

## Slide 2
<number>
Overview Video-related standardization in ITU-T & ITU-R
  Overview active bodies
  ITU-T SG9 & 12 – Video-related questions
  Tasks Q.13/12 & Q.14/12
Subjective quality assessment
Instrumental quality assessment
Overview

## Slide 3
<number>
Overview Video-related standardization in ITU-T & ITU-R
  Overview active bodies
  ITU-T SG9 & 12 – Video-related questions
  Tasks Q.13/12 & Q.14/12
Subjective quality assessment
Instrumental quality assessment
Overview

## Slide 4: Overview video-related standardization activities in ITU-R, ITU-T & VQEG
Institution
Part
Modality
Quality assessment

## Slide 5: Overview of ITU-T SG9 & SG12 Questions dealing with multimedia assessment
SG | Question | Title (shortened)
9 | Q.2/9 | Measurement & control of QoS for television transmission, contribution & distribution networks
 | Q.12/9 | Objective & subjective methods for audiovisual quality in multimedia services within terms of SG9
12 | Q.7/12 | Methods, tools & test plans for the subjective assessment of speech, audio & audiovisual quality
 | Q.9/12 | Perceptual-based objective methods for voice, audio & visual quality measurements in telecommunication services
 | Q.13/12 | QoE, QoS & performance requirements and assessment methods for multimedia including IPTV
 | Q.14/12 | Development of parametric models and tools for audiovisual & multimedia quality measurement

## Slide 6: Overview of ITU-T SG9 & SG12 Questions dealing with multimedia assessment
SG | Question | Title (shortened)
9 | Q.2/9 | Measurement & control of QoS for television transmission, contribution & distribution networks
 | Q.12/9 | Objective & subjective methods for audiovisual quality in multimedia services within terms of SG9
12 | Q.7/12 | Methods, tools & test plans for the subjective assessment of speech, audio & audiovisual quality
 | Q.9/12 | Perceptual-based objective methods for voice, audio & visual quality measurements in telecommunication services
 | Q.13/12 | QoE, QoS & performance requirements and assessment methods for multimedia including IPTV
 | Q.14/12 | Development of parametric models and tools for audiovisual & multimedia quality measurement

## Slide 7
<number>
End-user performance expectations for multimedia (esp. IPTV & Home Network)
Planning models end-to-end multimedia services
Performance monitoring methods (esp. IPTV & Home Network)
Quality management & assurance
QoE overview
Revisions of Recs. G.1010, G.1030, G.1040, G.1050, G.1070, & Y.1562
Q.13/12 Tasks

## Slide 8
<number>
P.NAMS – non-intrusive model, IP protocol information
P.NBAMS – non-intrusive model, IP protocol & bit-stream information
Q.14/12 Tasks

## Slide 9
<number>
Overview Video-related standardization in ITU-T & ITU-R
  Overview active bodies
  ITU-T SG9 & 12 – Video-related questions
  Tasks Q.13/12 & Q.14/12
Subjective quality assessment
Instrumental quality assessment
Overview

## Slide 10: Subjective multimedia test methods ITU-T & ITU-R standards
Video quality testing
  ITU-T Rec. P.910 (2008), e.g.
    ACR (Absolute Category Rating)
    ACR-HRR (ACR with Hidden Reference Removal)
    DCR (Degradation Category Rating)
  ITU-R Rec. BT.500-11 (2002), e.g.
    DSCQS (Double stimulus continuous quality scale method)
    DSIS (Double stimulus impairment scale)
  ITU-R Rec. BT.710-4 (1998), e.g.
    Specific methods for high-definition television assessment
Audiovisual quality testing
  ITU-T Rec. P.911 (1998), e.g.
    SSCQE (Single Stimulus Continuous Quality Evaluation)
Interactive systems
  ITU-T Rec. P.920 (2000)
    incl. conversation scenarios

## Slide 11
<number>
Overview Video-related standardization in ITU-T & ITU-R
  Overview active bodies
  ITU-T SG9 & 12 – Video-related questions
  Tasks Q.13/12 & Q.14/12
Subjective quality assessment
Instrumental quality assessment
  Overview
  P.NAMS/P.NBAMS
Overview

## Slide 12: Instrumental quality assessment
Subjective
quality-
rating
Transmission- System
Back- ground
Attitude
Mood
Experi-
ence
Motivation,
Goals
User-factors
…
Source video signal (SRC)

## Slide 13: Instrumental quality assessment Full Reference models – FR
Transmission- System
Source video signal (SRC)
Subjective
quality-
rating
Degraded video signal (PVS)
Model
Estimated quality index
Reference
Models
ITU-T J.144 (SG9)  SD  no transmission errors
ITU-T J.247 (SG9)  VGA, CIF, QCIF

## Slide 14: Instrumental quality assessment Reduced Reference models – RR
Model
Transmission- System
Source video signal (SRC)
Subjective
quality-
rating
Estimated quality index
Degraded video signal
Feature extraction
Reduced reference
Models
ITU-T J.246 (SG9)  VGA, CIF, QCIF

## Slide 15: Instrumental quality assessment No Reference models – NR
Model
Transmission- System
Source video signal (SRC)
Subjective
quality-
rating
Estimated quality index
Degraded video signal
Models
None standardized

## Slide 16: Instrumental quality assessment Bitstream/parametric models
Model
Transmission- System
Source video signal (SRC)
Subjective
quality-
rating
Estimated quality index
Bitstream / Parameters
Monitoring
P.NAMS (Q.14/12)
P.NBAMS (Q.14/12)
Planning
G.OMVAS (Q.13/12)
G.1070 (videotel. Q.13/12)

## Slide 17: Instrumental quality assessment Hybrid models
Model
Transmission- System
Source video signal (SRC)
Subjective
quality-
rating
Estimated quality index
Bitstream / Parameters
Models
VQEG Hybrid project
VQEG Joint Effort Group (JEG)
Degraded video signal

## Slide 18
<number>
Overview Video-related standardization in ITU-T & ITU-R
  Overview active bodies
  ITU-T SG9 & 12 – Video-related questions
  Tasks Q.13/12 & Q.14/12
Subjective quality assessment
Instrumental quality assessment
  Overview
  P.NAMS/P.NBAMS
Overview

## Slide 19: P.NAMS/P.NBAMS Application areas
Two application areas
QCIF-QVGA ("low bitrate mode", LBR)
  Linear Mobile TV over RTP (Mobile TV over a 3G mobile network with MBMS & with unicast, RTP/UDP/IP)
  Multimedia streaming (3GPP PSS, RTP/UDP/IP)
  Progressive download (e.g. HTTP/TCP/IP, [RTP/]TCP/IP)
SD and HD television ("high bitrate mode", HBR)
  Linear broadcast TV (MPEG2-TS/RTP/UDP/IP, MPEG2-TS/UDP/IP & RTP/UDP/IP)
  Video on-demand (MPEG2-TS/RTP/UDP/IP, MPEG2-TS/UDP/IP & RTP/UDP/IP)
  Progressive download (HTTP/TCP/IP, MPEG2-TS/TCP/IP or [RTP/]TCP/IP)

## Slide 20: P.NAMS/P.NBAMS ToR Modes of operation
NN mode
BN mode
CN mode
CC mode
XY: X = location of measurement (N: Network, C: Client, B: Both network and client)
Y = location of model (N: Network, C: Client)

## Slide 21: P.NAMS/P.NBAMS & error resilience Collaboration Q.14/12 & Q.17/12
FEC: Forward Error Correction
ARQ: Automatic Repeat reQuest

## Slide 22: Q.14/12 important dates
P.NAMS
Final announcement for proponents 28 June 2010
P.NAMS recommendation ready for consent 14 October 2011
P.NBAMS
Call for participation sent 17 Sept. 2010
Final announcement for proponents tbd
P.NBAMS recommendation ready for consent tbd 2012
Meetings
Q.14/12 Interim Meeting Berlin 15-17 Sept. 2010
SG12 18-27 Jan. 2011

## Slide 23: Instrumental quality assessment Taxonomy
Model input
  Parametric description of the video processing path
  Signals (processed video signal – PVS, source signal – SRC, …).
  Bit-stream (e.g., model may carry out decoding)
  Hybrid: Signals & bitstream
Model output
  Estimated MOS, other…
  Audio, video, audiovisual quality
Measurement of input information
  Online
  Offline
  Estimation
Mode of operation
  NN, BN, CN, CC
Target services
  IPTV, VoD, mobile TV, video-telephony, …
  MSTV, system integration solution, Open Source, …
  CIF, VGA, SDTV, HDTV, …
Model type
  FR, RR, NR
  Audio, video, audiovisual
Applications
  Video component testing (codecs, PLC, etc.)
  Planning networks and services
  Defining & verifying QoS classes and SLAs
  Monitoring service quality

## Slide 24: Standards instrumental MM quality assessment
 |  | Audio (A) / Video (V) | Audiovisual Quality
Signals | RR/NR | J.246 (SG9) | VQEG MM-project Ph.2
 | FR | PEAQ (A, ITU-R); J.144, J.247 (V, VQEG/SG9); “HDTV” (V, VQEG/SG9) | VQEG MM-project Ph.2
Para-meters | Planning | - | G.1070 (videotel.) G.OMVAS (Q.13/12)
 | monitoring | P.NAMS (A, V, Q.14/12) | P.NAMS (Q.14/12); P.NBAMS (Q.14/12)
Hybrid | NR/RR | VQEG (Hybrid project, JEG) | -
Output Information
Input Information

## Slide 25
<number>
Thank you for your attention!
Further information can be found under
www.itu.int/ITU-T/studygroups/com12