## Slide 1
<number>
ITU
(International Telecommunication Union)
ITU-T
(Telecommunication standardization sector)
Study Group 12
(Performance, QoS and QoE)
Overview of Speech Activities in ITU-T Study Group 12
QoMEX’10, Trondheim, Norway
Sebastian Möller Co-Rapporteur Q.8/12
Notes: <number>

## Slide 2
<number>
Overview
Speech-related questions
Subjective quality assessment approaches
Quality prediction approaches
Tasks of Q.9/12: Signal-based models
Tasks of Q.8/12: Parametric models

## Slide 3
<number>
Overview
Speech-related questions
Subjective quality assessment approaches
Quality prediction approaches
Tasks of Q.9/12: Signal-based models
Tasks of Q.8/12: Parametric models

## Slide 4
<number>
Speech-related Questions in SG 12 (1/2)
Question number | Question title
1/12 | Work programme, QoS/QoE coordination and bridging the standardization gap
2/12 | Multimedia performance considerations for IP gateways
3/12 | Speech transmission characteristics of speech terminals for fixed circuit-switched, mobile and packet-switched (IP) networks
4/12 | Hands-free communication in vehicles
5/12 | Telephonometric methodologies for handset and headset terminals
6/12 | Analysis methods using complex measurement signals incl. application for speech enhancement techniques and hands-free telephony
7/12 | Methods, tools and test plans for the subjective assessment of speech, audio and audiovisual quality interactions
8/12 | E-Model extension towards WB transmission and future telecom. and application scenarios

## Slide 5
<number>
Question number | Question title
9/12 | Perceptual-based objective methods for voice, audio and visual quality measurements in telecommunication services
10/12 | Transmission planning and performance considerations for voiceband, data and multimedia services
11/12 | Performance interworking and traffic management for Next Generation Networks
12/12 | Operational aspects of telecommunication network service quality
13/12 | QoE, QoS and performance requirements and assessment methods for multimedia including IPTV
14/12 | Development of parametric models and tools for audiovisual and multimedia quality measurement purposes
15/12 | Objective assessment of speech and sound transmission performance quality in networks
16/12 | Framework for diagnostic functions and their interaction with external objective models predicting media quality
17/12 | Performance of packet-based networks and other networking technologies
Speech-related Questions in SG 12 (2/2)

## Slide 6
<number>
Overview
Speech-related questions
Subjective quality assessment approaches
Quality prediction approaches
Tasks of Q.9/12: Signal-based models
Tasks of Q.8/12: Parametric models

## Slide 7
<number>
Subjective Quality Assessment Approaches
Recommendations under Q.7/12.
Rec. P.800: Main Recommendation
Rec. P.805: Conversational Speech Quality
Rec. P.810: Modulated Noise Reference Unit
Rec. P.830: Speech Codec Assessment
Rec. P.835: Speech Quality in Noise
Rec. P.840: Circuit Multiplication Equipment
Rec. P.85: Voice Output Devices
Rec. P.851: Spoken Dialogue Systems
Rec. P.880: Time-varying Quality
Suppl. 24 to P-Series Rec.: Interaction Parameters
[Handbook on Subjective Testing Practical Procedures]

## Slide 8
<number>
Overview
Speech-related questions
Subjective quality assessment approaches
Quality prediction approaches
Tasks of Q.9/12: Signal-based models
Tasks of Q.8/12: Parametric models

## Slide 9: Quality Prediction Approaches Speech transmission services.
Model
Estimated Quality Index
System
Parameters
Linguist.
Backgr.
Attitude
Emotions
Experi-
ence
Motivation,
Goals
User Factors
Subjective Quality Judgment
Transmission
System
Speech Signals

## Slide 10: Quality Prediction Approaches Taxonomy of prediction models.
Input information:
Signals
  one or two signals
  acoustic or electric
Parameters
Protocol information
Combinations hereof
Measurement of input information:
Online
Offline
Estimation
Output information:
Listening-only
  integral quality
  quality features
Conversational
Talking-only
Application area:
Planning
Set-up and optimization
Monitoring
Network type:
Narrowband
Wideband

## Slide 11: Quality Prediction Approaches Taxonomy of prediction models: Narrowband case.
 |  | Listening |  | Conversation | 
 |  | Overall Quality | Quality Feat. | Overall Quality | Quality Feat.
Signals | 1, el. | P.563 | Psychoac. Measures | CCI (P.562) | 
 | 1, ac. |  | Psychoac. Measures |  | 
 | 2, el. | P.862 P.OLQA | P.AMD/ P.TCA | P.CQO? | P.CQO?
 | 2, ac. | P.OLQA | P.AMD/ P.TCA |  | 
Protocol | Meas. |  |  | P.564 P.CQO? | P.CQO?
Parameters | Estim. |  |  | G.107 | 
 | Meas. |  |  | NIEM (P.562) | 
Output Information
Input Information

## Slide 12: Quality Prediction Approaches Taxonomy of prediction models: Wideband case.
Output Information
Input Information
 |  | Listening |  | Conversation | 
 |  | Overall Quality | Quality Feat. | Overall Quality | Quality Feat.
Signals | 1, el. |  | Psychoac. Measures |  | 
 | 1, ac. |  | Psychoac. Measures |  | 
 | 2, el. | P.862.2 P.OLQA | P.AMD/ P.TCA |  | 
 | 2, ac. | P.OLQA | P.AMD/ P.TCA |  | 
Protocol | Meas. |  |  |  | 
Parameters | Estim. |  |  | WB-E-Model | 
 | Meas. |  |  |  | 

## Slide 13
<number>
Overview
Speech-related questions
Subjective quality assessment approaches
Quality prediction approaches
Tasks of Q.9/12: Signal-based models
Tasks of Q.8/12: Parametric models

## Slide 14
<number>
Tasks of Q.9/12
Overview.
New model for overall speech quality (P.OLQA)
New models for degradation decomposition (P.AMD, P.TCA)
New model for prediction of P.835 scores (P.ONRA)
Methods for talking quality prediction
Models for audio signals (e.g. music) transmitted over telecommunication links like GSM or VoIP
Models for synthesized speech quality
Models for video quality (restriction to low bit-rate coding and limited image sizes)

## Slide 15: Quality Prediction Models Signal-based models.
Reference-based approach:
Transmission
System
Pre- Processing
Pre-Processing
Internal
Represent.
Distance
Average
Transform.
x’(k)
Internal
Represent.
Clean speech
signal
y(k)
y’(k)
MOS
(e.g. ITU-T Rec. P.862, 2001; Hauenstein, 1997; Hansen & Kollmeier, 1997)

## Slide 16: Quality Prediction Models Signal-based models.
Internal Representation:
(Hauenstein, 1997)
Filter
Bank
x‘(k)
x2
TP
Power
Excitation
Specific
Loudness
Compression
Spectral
Masking
Temporal
Masking

## Slide 17: Quality Prediction Models P.OLQA, P.AMD and P.TCA.
Transmission
System
Internal
Represent.
Internal
Represent.
Pre-
Processing
Pre-
Processing
Comparison
Integration
Transform.
Noisiness
Indicator
Coloration
Indicator
Loudness
Indicator
Discontinuity
Indicator
(Côté 2010; Wältermann et al., 2008)

## Slide 18: Quality Prediction Models Multi-dimensional approaches.
F1
F2
F3
indirect, dark
direct, bright
interrupted
continuous
not noisy
noisy
F1: Directness/
frequency content
F2: Continuity
F3: Noisiness
(Wältermann et al., 2006)

## Slide 19
<number>
Overview
Speech-related questions
Subjective quality assessment approaches
Quality prediction approaches
Tasks of Q.9/12: Signal-based models
Tasks of Q.8/12: Parametric models

## Slide 20
<number>
Tasks of Q.8/12
Overview.
Wideband and mixed-band transmission scenarios
Terminal equipment other than standard handset telephones (e.g. HFTs, headsets)
Degradations introduced by speech-processing devices (e.g. EC, VAD, NR)
Use of the E-model for quality monitoring
Perceptual dimensions other than “impairment”, i.e. “speech sound quality” and conversational quality
Additivity property of the E-model
Coverage of user expectation, development of user expectation over time

## Slide 21: Quality Assessment and Prediction E-model for narrowband networks.
Backgr. noise, acoustic
coupling
Linear distortion, delay
Codec
Packet loss
Jitter buffer,
VAD
Talker echo,
listener echo
Circuit
noise
Backgr. noise, acoustic
coupling
IP WAN

## Slide 22: Quality Assessment and Prediction E-model for narrowband networks.
IP WAN
Overall quality R = Ro - Is - Id - Ie,eff
Estimated user judgment MOS = f (R )
Impairments SNR simultaneous delayed nonlin./timevar.
Ps, Ds,
STMR
SLR, RLR, Ta
Ie, qdu
Ppl
Bpl
TELR, T,
WEPL, Tr
Nc, Nfor
Pr, Dr,
LSTR

## Slide 23: Quality Assessment and Prediction E-model extension for wideband networks.
(Raake, 2006; Appendix II, ITU-T Rec. G.107, 2006)
Ro,max = 129

## Slide 24: Quality Assessment and Prediction E-model extension for wideband networks.
Ref. | Operating rate kbit/s | Ie,wb value
G.722 | 64 | 13
 | 56 | 20
 | 48 | 31
G.722.1 | 32 | 13
 | 24 | 19
G.722.2 | 23.85 | 8
 | 23.05 | 1
 | 19.85 | 3
 | 18.25 | 5
 | 15.85 | 7
 | 14.25 | 10
 | 12.65 | 13
 | 8.85 | 26
 | 6.6 | 41
G.711 | 64 | 36
G.728 | 16 | 43
G.729 | 8 | 46
G.729A + VAD | 8 | 47
IS-54 | 8 | 56
GSM 06.10, FR | 13 | 56
GSM 06.60, EFR | 12.2 | 41
G.723.1 | 5.3 | 55
G.723.1 | 6.3 | 51
Ro,max = 129
(Raake, 2006;
Möller et al., 2006)
AMR-WB (23.05)
AMR-WB (6.6)

## Slide 25
<number>
Thank you for your attention!
Further information can be found under
www.itu.int/ITU-T/studygroups/com12